## Slide 1: PVT Manager Test Leader Training

## Slide 2: PVT – Performance Validation Test
Verify and Validate functionality in a truck from a driver perspective
  Verify – the driver manual
  Validate – with experienced drivers
Corresponds to many very demanding customers using ALL functionality in the complete vehicle

## Slide 3: Test Structure Hierarchy
PVT
Truck Function Area
Truck Function Area
Truck Function Area
Truck Function Area
TestCase
Function
Function
Function
Function
TestCase
TestCase
TestCase
Categorization
- Slightly connected to Commodities
11
-Easy to understand
-”Stand alone”
- Component independent
170
-Here is where the VehicleSpec meets functions!
-The VARIANT controls which components!
1000

## Slide 4: The Atomic PVT
Smallest piece in building a PVT is the test case!
From that we can generate statistics and results with several different views
Executing test cases is sequential testing and used for verification.
But it is actually what happens in between the testcases that is important when we are validating a product. For that, experience from the product usage is critical.

## Slide 5: Testcases vs Functions and testcoverage
F#1
F#6
F#1
F#4
F#6
F#1
F#4
F#6
F#1
F#4
F#6
F#1
F#4
F#6
F#1
F#4
F#6
F#1
F#6
F#1
F#2
F#4
F#6
F#1
F#2
F#3
F#4
F#6
F#1
F#2
F#3
F#4
F#5
F#6
F#1
F#2
F#3
F#4
F#5
F#6
F#1
F#2
F#3
F#4
F#5
F#6
F#1
F#6
F#1
F#2
F#4
F#6
F#1
F#2
F#3
F#4
F#6
F#1
F#2
F#3
F#4
F#5
F#6
F#1
F#2
F#3
F#4
F#5
F#6
F#1
F#2
F#3
F#4
F#5
F#6
F#1
F#n
F#1
F#2
F#4
F#n
F#1
F#2
F#3
F#4
F#n
F#1
F#2
F#3
F#4
F#5
F#n
F#1
F#2
F#3
F#4
F#5
F#n
F#1
F#2
F#3
F#4
F#5
F#n
Test Width
Test Depth
Test environment
box
= One testcase for a Function
Road Conditions
Weather Conditions
Endurance
Regional
Country
External equipment
Functions
TC/Function

## Slide 6: Formal Truck Function Verification & Validation PVT CHECK
box
= One testcase for a Function
One testcase/Available functions
Very high level testing
~8h/truck
Finds stoppers in all available functions
Used for delivery control

## Slide 7: Formal Truck Function Verification & Validation PVT TOTAL
box
= One testcase for a Function
ALL testcases/Available functions
Dig deep!
~4weeks/truck
Exercise and challenge complete system
Most thorough Formal Verification

## Slide 8: Formal Truck Function Verification & Validation PVT Base
box
= One testcase for a Function
HALF of all testcases/Available functions
Dig pretty deep!
~2weeks/truck
Exercise and challenge complete system
”Normal Use” Formal Verification
Missing from TOTAL is:
Measurements! (In Base we trust the system, eg. Fuel level)
Sleep over!
Timeconsuming testcases
Jeopardize the system
Parameter changes
Diagnostics
Jinx the system

## Slide 9: Truck Function Validation PVT Europe
box
= One testcase for a Function
Most used functions during normal use are tested in several different environments. ~6weeks/truck
Environmental factor:
Countries
Road conditions
Traffic situations (Ferries, tunnels, traffic jams etc.)
Climate changes
Sleepover at truck stops
Using experiences from drivers
Validation test when product is mature enough

## Slide 10: Truck Function Validation PVT Haulage
box
= One testcase for a Function
SOME functions with several testcases are tested in different environments on a high level.
~6weeks/truck
Requirement on mileage.
Environmental factor:
mileage
Validation test when product is mature enough.

## Slide 11: Truck Function Verification & Validation PVT Development
box
= One testcase for a Function
Custom Built test
Any test that the TestRequester orders
Using a PVT Check for regression testing
Normally used early in projects to evaluate a single project in a truck

## Slide 12: Vehicle Spec for a certain test PVT TOTAL
12
2013-03-06
box
= One testcase for a Function
Adding Vehicle Spec to a test will remove Functions and Testcases from the test.
Function coverage
Testcase coverage .
= Test Coverage (Relative Variant coverage)
Function not available
Testcase not available

## Slide 13
Function and maturity growth
Verification
Development
Validation
PVT Base
PVT Check
PVT Total
PVT Total
PVT EU
PVT Haul
PVT City
PVT Cons
PVT EU
PVT Development
Support project development with high project focused tests
First formal verification with a few trucks, low spec
Heavy formal verification,
Many trucks,
High spec
Validation!
Project activities
PVT activities
Chain of rising PVT
PVT Dev: only development
PVT Check: First formal verification
PVT BASE/TOTAL: Heavy Verification
PVT HAUL: Verification and Validation
PVT EU: Only Validation

## Slide 14: Foundations of PVT
TR
Test Request – The Customer and a desire
Test Engineer that can transform a request to a test
A test engineer is the interface between; the projects, the vehicle, the drivers, the logging equipment, the desire, the reports and the result.
Tools that supports all logging needed to generate a good result
A tool suite that supports all needs in executing all kinds of different tests.
Experienced Drivers -
Dedicated and devoted to their job
The foundation of product validation! People who knows how to use the product
Test system that supports both flexible and structured testing
A Test Structure Hierarchy that generates statistics and support conclusions without loosing the creativity to test.

## Slide 15
PVT Test Code
New SW Loop
ER-Report
Verification test of driver manual &
Validation test of software functionality from a driver perspective
Truck Function Validation (PVT - Performance Validation Test)
Development of E-FACTS
Protus
Verification
In vehicle
logger
Local Data Collector Raw Data
Data Refiner App.
(Not for PVT Check)
Truck Function
Status

## Slide 16: Lessons Learned from site Lyon
Presented by Julien Rouge Lyon TFV Manager

## Slide 17: Lessons learned from Lyon
Networking is crucial, securing understanding & acceptance by:
  Direct contacts within the fault resolution process (local specific processes e.g. ”PATI”)
  Testing organizations (RT/AET/FT)
  Engineering
  Project people (FVV-PMO, Product PM…)
  Features ==> ”FVV one voice”
  Brands
Renault adaptation of the test cases was the biggest work
E-FACTS was quite well prepared for Lyon usage

## Slide 18: Lessons learned from Lyon
Aim for the fastest possible team set-up:
  Work the right way from the start, don’t cope too much
  Look for a PVT Tester from the start (difficult to find, long to educate)
  Drivers training:
    Educate drivers in truck functionality & technology (Bluetooth phones…)
    Then proceed to PVT testing
  Synch work with GOT for speed & support (weekly in the beginning…)

## Slide 19: Lessons learned from Lyon
Recruitment process issues:
  It takes a long time to find the right people
  Internal transfer can take a long time (6 months for TE)
  The company economic status influences recruitment a lot
Implementation financing:
  A PIM project is not so bad, yet a lot of Presentations to prepare, requiring help from a experienced PM
  P2683 also participated a lot to the cost
IT data transfer rate from proving ground can be an issue

## Slide 20: Plan to implement PVT at other sites
Presented by Martin Svennungsson

## Slide 21: PVT at other site
PVT
Drivers
From Driver Team
SW Offer & Telematics
Responsible
PVT
Tester
PVT
Test Engineer
PVT
Developer
Global TFV Coordinator
GSO
CUR
PVT Planning Responsible
PVT
Performance Validation Test
BF59990 TFV
HPG & Lundby
Truck Function Specialist
BF59991 TFV
LVPG & St Priest
PVT Trouble Shooter
TFV System Architect
TFV Applications and Tools Local Super User
E-FACTS Applications &
Tools

## Slide 22: PVT ramping phases - Overview
Start-up phase
Learning phase
Execution phase
Evaluation phase
Operational
Learning routines
Networking
Visits
Project Sync
Infrastructure - IT - Testtracks - Equipment
Planning
Recruitment
Learning Truck Functions
Learning testcases
Developing testcases
Learning Brand culture
Evaluate cultural differences
Testrun on PVT Total
First real PVT for needed projects
Evaluate learning and execution
White book
Adapt
Document
Implementation Phase
Draft

## Slide 23: PVT ramping phases - Gates
Start-up phase
Learning phase
Execution phase
Evaluation phase
Timeplan
Budget
Infrastructure
Roles
Resurces
Testtracks
Handshakes
Visit PVT Total in GOT
All roles have education and know what is expected from them
Test code OK status
Operational
Decided by Continental Manager PVT/ Global TFV Coordinator /Truck Function Specialist
Are we mature enough?
Are every TC understood and have a result
Draft
Implementation Phase

## Slide 24: PVT Test Proces

## Slide 25: PVT Manager - Purpose
Database for all Test Cases
Database for Test Sequences
Tool to generate Reports
Tool for Vehicle Planning
Adminitration tool for users and content
All questions – Send mail to ”Application E-FACTS”

## Slide 26: PVT Manager Access Level
 | Test Leader | SE | ME | Tools | Adm
PVT Test Case Editor | View, CR, New | View, CR, New | Full |  | Full
TFA/TF | View | View | Full |  | Full
Test Sequence | View, Export | View, Export | Full |  | Full
Vehicle Planner | View | View | Full |  | Full
Vehicle Specification | View | View | Full |  | 
Reports |  |  |  |  | Full
Tool Box |  |  |  | x | Full

## Slide 27: PVT Test Case Editor
Truck Function Area vs. Truck Functions vs. Test Case
Test case content – Product Class/Specification/Test method
Change Request or New test Case
Excel Printout
Filter and search for TC
SPEC ! = NOT, I = OR, && = AND
ProductClass $ = AND

## Slide 28: Send a Test Case Request

## Slide 29: PVT Test Sequences
Different PVT Test Methods
Typical Test Routine for the PVT Test Methods
Default Test Sequences
Custimized Test Sequences
Export Test Sequences
Test Leader Feedback to Site/Master Editor about problems found

## Slide 30: Truck Function List Editor
Handles all Truck Functions and Trucks Function Areas
Gives short information about the Truck Functions
(Some mismatch in PROTUS, due to delay)

## Slide 31: Reports
Only valid PVT trucks/SW are in the list
  Ordered by mail to ”Support E-FACTS”
Individual Truck Report
Total Truck Function Report (need to be handled in Refiner first)
E2E Function Report
Compare SW package
Truck Function Consistency
Test Case Consistency
Currect Test Coverage

## Slide 32: Reports

## Slide 33: Reports – Individual Report

## Slide 34: Vehicle Localizer
Showed the position for the last uploaded GPS data
Today PAUSED, due to future RDM possibilities

## Slide 35: Vehicle Localizer

## Slide 36: Vehicle Specification
Search and show Specification inside eFACTS
Should be updated once a month from PROTUS, total file
Should be updated every day from PROTUS for changes

## Slide 37: Vehicle Specification

## Slide 38: Vehicle Planner
Tool to support Project to select trucks
Can also be used to check
  Test Case Coverage
  Test Function Coverage - Test Depth
  Test Confidence

## Slide 39: Vehicle Planner

## Slide 40: Tool Box
Administration of
  Move data to correct truck
  Import Vehicle Specification from PROTUS
  System Parameters
    Users
    SW versions
    Status report PVT items (Vehicle/SW)
    Mail contact
  Measurement Topics

## Slide 41: Tool Box - GUI

## Slide 42: Refiner usage for PVT
Test Leader access level needed to handle results from PVT Testing.
Truck Function Status Report
Report fault against Test Cases

## Slide 43: Job list (for Site and Master Editor)

## Slide 44: Weekly TFV Status Report – Delivered by GOT today
Example