## Slide 2
Logged data
CAN trafic, Audio / video, GPS, snapshot
PROTUS
QUEST/ (EEE)
SW Release Function Package FP
Update
The new way! RT/PVT/FT (AET)
I have logged an error !
The driver perspective!

## Slide 3
How to start the logger manually?
The microphone LED shows a blue light  system is ready
An error occurrs  the driver presses the button logging starts  LED shows a yellow light
  Traffic is logged on up to 12 CANbuses (25 s BEFORE and 15s to 2 min AFTER the button is pressed)
  Audio Commentary is recorded 15s-2 min AFTER the button is pressed
  Video/picture (e.g. cluster/road information), 10s before button is pressed and 15s to 2 min after.
Trigger start button
Yellow light– logging in progress
Microphone
/!\ Wait 1 minute between 2 successive logs
Pressing the button while yellow LED extends recordings

## Slide 4
DO019999.dat
Signal based measurements (eFACTS -> ”Snapshot data”).
All events in the same file.
One ”DOxx-file” for each ”Storage Group”
DO019999_x.csv
Converted event from storage group 1 with ”split trigger” attribute
T010019999.bin
CAN Traffic measurement.
Max 6 Traffic Groups
All CAN buses in same file
One file for each event
A010019999.wav
Audio measurement.
One file for each event.
No storage groups
V010019999.avi
Video measurement.
One file for each event.
1 USB Camera -> avi file format
1-4 cameras in video extender -> h264 file format
Video extnder files donloaded seperately
No storage groups
BDU_files
Response files from UDS jobs
CAN
SIGNALS
TRAFFIC
ASYNCHRONOUS
SYNCHRONOUS
A010019999.dat / V010019999.dat
Synchronization files for Audio resp. Video

## Slide 5
eFACTS Application Server
WCF Services for database interface (Oracle, NHibernate)
Organizer
Converter
External Services
Remote Collector
TruckSpec_Update
Database_Backup
Process Watchdog
FTP Server for ”Assist Me”
FTP Server for data download.
Collector
Data Refiner
External Data Import
WEB Search Tool

## Slide 6
COLLECTOR (REMOTE)
Data integrity checks
Storage Group Validation
Split Measurement types
Parse UDS files (BDU)
RAW
External
Auto_Traffic
Data
ORGANIZER
Back-Up
Repacking RAW data
Creating Event Data Packages
Manage Auto-traffic measurements
Checking in data
Delete completed measurements
Send weekly statistics
CONVERTER
Convert data files to different formats
Create data package for ”Assist Me” FTP server
Transfer
External Data Import
Download external data
Convert to several formats
WEB Search Tool
Search data by keys
Database Backup
External Services
TruckSpec_Update
EDB

## Slide 7
PC Collector
Server Collector
RAW
Server Applications
DATA
External
External Data Import Tool
Data export to
Safety, Poolman, ...
RDM
AutoTraffic
PC Collector
Server Collector
RAW
Server Applications
DATA
GTDM
RDM
AutoTraffic ?
Data export to
Safety, Poolman, ...