## Slide 1: Introduction to eFACTS Logging 2014-03-28
Martin Svennungsson/Jonas Qvist/Markus Löfgren/Jean-Philippe Abeillon
Notes: JPA – additional changes:
Replacement of Volvo 3P by Volvo GTT

## Slide 2: Agenda
Background
What is Truck Function Validation ?
Way of working (Yesterday/Today)
The data logger
How to use the logger system
Installations
How to handle logged data
Data Management Applications
Demo of applications
(PC installations)

## Slide 3: Evolution of the E/E-Architecture
Airbag
EPS
4WD
ABS/ESP
Transmission
Engine
ACC
door driver
door passenger
Rear door right
Rear door left
wiper
Radio
phone
AMP
Navigation
TV
climate
Seat driver
Seat passanger
PTC
PDC
Dome Lamp
ReLi.Sens.
gateway
phone
AMP
IP
radio
Infotainment CU
access control
cab extension
door module
HFAC
Cabin CU
DAS
level control
BMS
TPM
Chassis CU
retarder
transmission
brake
EMS
Powertrain CU
Standalone ECUs
Linked ECUs
Multi Function ECUs
Cluster ECUs
Backbone BUS
Decentraliced Gateways
Intelligent Sensors/Actuators
Heterogeneous BUS system
Central Gateway
Integrated ECUs
Single BUS system
Function specific ECUs
Function specific ECUs
Signals shared via splicing
TEA
TEA2
TEA2+

## Slide 4: Architectural Differences
Vehicle Architecture
  The J1587 data link has reached its limitation.
    No support for old platform component from suppliers
    Not an industry std.
    Very slow SWDL (not meeting GM/AM reqs)
  Limitations for added functionality.
    Pass Through
    Infrastructure
Cab Architecture
  Centralised EE architecture in CAB (IC, LCM)
  All Switches Hard wired (~5pins/switch)
  Two pass through (~600 pins)
Chassis architecture
  Sensors and actuators on chassis
  W/H routed on both right and left (mixed with pneumatics)
Manufacturing
  Current product is not modularized and the assembly has a huge complexity in the area of clipping and routing
  Every truck are more or less unique and the assembly quality is to a very high extent operator dependant
TEA2
Vehicle Architecture
  J2284 500kbit Volvo proprietary net (CAN)
  Separation of infrastructure and application (Autosar)
  Following industry standards and interfaces
    ISO Diagnostics, Std protocols, A-interfaces GIC
Cab Architecture
  Distributed EE architecture in CAB (Gateways)
  Flexible Switch concept (3pins per 4 switches)
  One pass through (155pins)
Chassis Architecture
  ECUs on chassis
    Less W/H part no and less terminals
  W/H always mounted on the right side of the frame, avoiding mixing with pneumatics
Manufacturing
  Modularized product with easier clipping and routing
  Assembly time. Faster communication needed to reduce assembly time. Since software sizes will increase this will be even more important
TEA2+
Notes: JPA – minor typing modifications
Additional changes – “Add-on differences”
New enhanced diagnostics (supporting new demands of Soft offers, due to enhanched diagnostic capabilities)
New aftermarket tools (improved GD)
New power management strategy (enhanced battery lifetime, optimized power consumptions in different vehicle modes)
New communication strategy (faster SWDL, allowing distributed system to be able to modularize the EE architecture)
New processes and development tools (to have a faster time to market, and portability)

## Slide 5: Add-on Features with TEA2+
New Enhanced Diagnostics
  Support of new Soft Offer demands thanks to enhanched diagnostic capabilities.
  New aftermarket tools (improved GD)
New Power Management Strategy
  Enhanced batteries lifetime
  Optimized power consumption thanks to several vehicle modes
New communication strategy
  Faster Software downloads
  Allows distributed system to be able to modularize the EE architecture
New processes and development tools
  Faster time to market
  Portability
Notes: JPA – New slide

## Slide 6: TEA2 Architecture
STD
MCC
CAN-4:
SAE J1939
J1939-1
J1708/J1587
LCM
SA:55, MID:216
ESP
EBS
ABS-F
ABS-B
SA:11, MID:136
GSECU
SA:5, MID:223
IMMO
MID:163
SRS
MID:232
ECC
MID:146
B-builder
VCADS
MID:172
Phone
SA:74, MID:231
Audio
SA:76, MID:206
Cluster
SA:23, MID:140
ECS
SA:47, MID:150
J1939-3
Alarm
MID:214
J1939-7
EMS II
SA:0 (15), MID:128
OBD scan tool
SA:249, 250
FMS-GW
SA:37, MID:179
CAN-EXT:
SAE J1939
BBM
SA:230, MID:249
TECU/GSECU for
- AMT-C
- PowerTronic
J1939-6
LPS
SA:232, MID:248
TTU
MID:203
J1939-2
USB
TPM
SA:51, MID:166
NOX
SA:81
ADS
SA:61, MID:233
RAS
SA:56, MID:184
ALCOLOCK
SA:-
T-GW
SA:65, MID:141
EGR
SCR
ISO 11992-2
Trailer connection
LCS
SA:174, MID:204
VECU
SA:17, MID:144
J1939-8
ACC Radar
SA:42, MID:219
DACU
SA:173, MID:238
TECU
SA:3, MID:130
Tachograph
SA:238, MID:220
UQS
SA: 163
VGT SRA
SA: 2
RECU
SA:16, MID:222
NOX
SA:82
Notes: Centralized functional allocation
  Little segmentation
  All communication via backbones,
    SWDL, Diagnostic and some functional signals on J1587
    Primarily functional data on 1939

## Slide 7: TEA2+ HD COE Architecture
Notes: Distributed functional allocation
  Network is segmented into several sub-nets, e.g. chassis
    Efficient utilization of communication bandwidth and harnesses
  Only “necessary” communication on backbones, feature communication on subnet i.e a segmentation.
  Gateways
    Connects the main network segments
    Performs routing
    Provide a central diagnostic connection
  Cooperation with suppliers on complete sub-nets
    Minimized need for coordination resources from PD

## Slide 8: LIN (Local Integration Network)

## Slide 9
”Truck Function Validation” Background
Historically, Complete Vehicle / FVV has focused on mechanical testing.
For the new electrical architecture TEA2+, a new structured way of working is needed to include EEE in the complete vehicle testing from a driver perspective.
Earlier, no logging was made when a electrical faults appeared. You have simply reported the error in Protus and left to EEE to handle the fault tracing.
  The lead time for solving electrical problems needs to be shortened.
  Occasional errors are hard to recreate. Logging always needed.
  Earlier, electrical testing has mostly been ”happy testing”.PVT testing and integration of electrical testing in RT/AET/FT codes needed.

## Slide 10: What has Truck Function Validation accomplished?
New test code - Performance Validation Test (PVT)
  Translated functional specifications into test code.
  Tested PVT and logger equipment in vehicle.
Updated the test codes for RT/AET/FT
Provided a new data logging system including:
  New hardware
  Developed a ”back office” solution for data management.
  New way of storing data files (cheaper)
Upgraded Protus to support web-links
Improved the network against EEE
Ensured TEA2+ education for CV
New TeamPlace

## Slide 11: Old way of working
PROTUS
No logged data
Software update
”I got a problem !”
EEE Rescue Team
In vehicle fault tracing
(not always successful)
Notes: JPA – addition of RT trucks

## Slide 12
Logged data
CAN trafic, Audio / video, GPS, snapshot
PROTUS
QUEST/ (EEE)
SW Release Function Package FP
Update
The new way! RT/PVT/FT (AET)
I have logged an error !
The driver perspective!

## Slide 13
Why do we need a new system?
Then:
Earlier, measurements have been focused on separate functions.
You have known which signals to log.
The functions have been more or less unique for each ECU.
Now:
We don’t know which errors that will appear = we don’t know what to log.
Functions distributed over several ECU’s = we don’t know which data buses to connect to.
We don’t always know what is the cause and effect = we don’t know which signals to log.
Conclusion:
Connect everywhere and log everything!
Consequence:
Large amount of data that have to be sorted by fault types and made accessible to the end users.
Solution:
1. New logging equipment that meets the new demands.
2. New ”Backoffice” solution for data management.

## Slide 14: DEMO

## Slide 15: System Installations
Must have:
  Breakout cables CAN
  Power cables +24V, Gnd, ignition
What to connect ?
  CAN, Power
  Place the microphone + GPS (+ video)
To verify the installation CANalyzer is needed.
To test the installation on a later stage, use CVEL_MLOG_Tester.
  Run the application on the USB-stick to verify CAN-traffic (CVEL_MLOG_Tester) – if you have log files from several loggers you have to choose which logger to test It is always the latest log file that is being cheked, snapshot data included.
  Regarding video, use the PC to configure the camera.
NOTE: You have to register in the database in which vehicle the logger is installed. Use the Collector application the configure.
  In a near future this action becomes obsolete. The logger will read information from vehicle.

## Slide 16
How to start the logger manually?
The microphone LED shows a blue light  system is ready
An error occurrs  the driver presses the button logging starts  LED shows a yellow light
  Traffic is logged on up to 12 CANbuses (25 s BEFORE and 15s to 2 min AFTER the button is pressed)
  Audio Commentary is recorded 15s-2 min AFTER the button is pressed
  Video/picture (e.g. cluster/road information), 10s before button is pressed and 15s to 2 min after.
Trigger start button
Yellow light– logging in progress
Microphone
/!\ Wait 1 minute between 2 successive logs
Pressing the button while yellow LED extends recordings

## Slide 17: How to turn off the vehicle?
The logger is activated when ignition is turned on.
The logger closes down 30 s AFTER ignition off.
The microphone LED quickly flashes red/blue when packing files.
WAIT until no microphone LED light is turned on, before you turn off the vehicle main power switch/lock with the remote.
  In effect, wait about 30 s after you have switch the ignition off.
  This is a general rule for all measurement systems.

## Slide 18: How to transfer data from the logger using a USB memory stick?
I possible, only use CORSAIR Voyager USB-memory (16GB)
  They have a faster transfer rate, recommended by the supplier.
Insert the memory stick.
Look at the microphone LED
  It will change from blue to red and after a while flash fast between red and blue (the data is being zipped)
  It will change from blue to red and after a while flash slowly red and blue (the data is being transferred to the stick)
  NOTE ! No data remains in the logger ! (configurable)
After the LED showed STEADY red light at least 10 s, the transfer is ready. Check also that the USB stick LED is off.
Pull out the memory stick
  The LED will turn blue again.
If nothing happens when the stick is inserted, check the extension cable!

## Slide 19: How to get data from several loggers?
You can get data from several loggers in the same way as one.
The data structure on the USB-stick will be:
  8000xxxx
  8000yyyy
  8000zzzz (one folder per M-LOG datalogger serial number)
You can also provide the stick with a security key – without the right key you are not able to transfer data.
(If you want to change the logger configuration you can use the memory stick.).

## Slide 20: Extra: Log file structure
8000xxxx
  DATA
    LOGxxx.zip (information about the device, a new file is created for every ignition on/off, always remains)
    MEAxxx.zip (a new file is created for every ignition on/off, only remains if there is logged data)
      Traffic (one for each event)
      Audio (one for each event)
      Video (one for each event)
      Data (”external data” or snapshot data)
  DEVICE
    Current configuration
Volvo GTT Martin Svennungsson / Jonas Qvist / Markus Löfgren / Jean-Philippe Abeillon
Notes: Slide 23 removed because it is already present in the EFACTS education Presentation

## Slide 21
In Vehicle
Logger System
Local Data Collector
Raw Data
Data Transfer Via USB,
Ethernet, WLAN or 3G.
Data Refiner App.
Volvo IT
Oracle DataBase
Key/Meta Data
End Users
Automated Upload
CVEL Data System
Application Server
WEB Search App.
System Service
Converter Service
Mass Storage
(Net Disc)
Test Administrator
Search Parameters
Data. (CANalyzer format)
Adding search keys and comments

## Slide 22: My responsibilities as TE/TL
Check/update - logger/vehicle binding in Collector
Transfer the data from the logger to the server.
Check-in Events to the database with appropriate keys attached. 30 day limit from when event was recorded!!
Discard non-valid Events
Link the data to a PROTUS report.
Volvo GTT Martin Svennungsson / Jonas Qvist / Markus Löfgren / Jean-Philippe Abeillon

## Slide 23: Application Demo
Volvo GTT Martin Svennungsson / Jonas Qvist / Markus Löfgren / Jean-Philippe Abeillon

## Slide 24
http://cveldata.got.volvo.net/Default.aspx?ProtusGUID=7d521104-a737-4e68-9f74-924d098b0a4b
Encrypted PROTUS Id
PROTUS link

## Slide 25: PROTUS

## Slide 26: Work flow - repetition
Upload data from logger
Check Logger/Vehicle binding in Collector
Copy data from USB to C:\MeasData (everything incl 8000xxxx)
Also save a copy somewhere on your local HDD
Wait until all data on USB is in the MeasData folder
Upload data to server using Collector (Transfer window)
  Note! Transfer rate, when working outside Volvo
  ”Show Log-file..” (if correct MEA_xxxx and usually LOG_xxxx)
Refine data –(add metadata+Check-in) or Discard, using Refiner
Create PROTUS link in Refiner, identical info in PROTUS id as you entered, when creating the link
Upload the link in PROTUS
Check that the PROTUS link works.

## Slide 27: Future Developments
Readout of the vehicle id (VIN)
Diagnostics readout
Remote communication (WLAN)
  ”Hotspots”
Display
  RT-testing (brake temp/warning, …)
Multiple LIN
Readout of the ECU HW/SW id
Remote communication (GPRS/3g)
  Transfer data
  Change configuration
Futher camera implementations
  Max 4 , against the light, darkness

## Slide 28: Future Workflow
PVT Manager
eFACTS Refiner
Test Sequence
Import Test Sequences
Export Results
Editing Test Cases
Managing Test Sequences
Creating Reports

## Slide 29: PC Prerequisites
”Open Client” for myPlace computers (FAROS)
  First mail to Martin (GOT users)
  When confirmed, use motivation sent by Martin (GOT users)
Oracle client version 11 or newer (FAROS)
Contact TFV team for installation or use
  eFACTS Data Refiner
  eFACTS Collector
  CVEL USB Applications (if needed)
    CVEL_Data_Copy, CVEL_MLOG_Tester, CVEL_USBauto

## Slide 30: Introduction to eFACTS Logging
Questions? Mail to: support.efacts@volvo.com
Logger problem (GOT): +46 31 32 73090
https://teamplace.volvo.com/sites/3p-EEE-CV/default.aspx